## Slide 1: FIELD INVESTIGATION OF IN SITU LIME NEUTRALIZATION OF ACIDIC SEDIMENT
John Villinski
SME 2017 Annual Conference
Denver, Colorado
February 22, 2016

## Slide 2: Problem
Alluvial aquifers impacted by past mining operations
Majority of the acidity and metals stored in the sediment
  Estimates of pump & treat cleanup times can many decades
Notes: This is pretty well known, just to set the stage
Unlined tailings, pond upsets, improper storage of process solutions

## Slide 3: Program Objectives
Evaluate treatment alternatives to enhance remediation and shorten duration
  Effectiveness
  Implementability
  Cost
Proposed Technology – in situ neutralization with alkali
Notes: This talk will focus on effectiveness and implementability
Other treatment options – oxidation, sulfate reduction/sulfide precipitation, etc.

## Slide 4: Field Testing
Infiltrate lime solution via basin to acidic sediment at base of vadose zone
Implementability
  mix and infiltrate near-saturated lime solution
  control solids
  avoid application facility/aquifer formation damage
Effectiveness
  raise pH (target pH 8)
  reduce metals concentrations

## Slide 5: Field Testing
Alkali treatment is a two-step process
  Alkali application
  Neutral water flush
Targets
  Deliver alkali dose over 5 days
  Transport alkalinity through treatment volume

## Slide 6: Acidic Vadose Zone Test Schematic
Treatment Volume
Circum-neutral Vadose Zone
CNVZ
pH > 6.5
Acidic Vadose Zone
AVZ
pH < 6.5
MWVZ01
Bedrock

## Slide 7: Pretest Sediment pH Cross Section
CNVZ
AVZ
ASZ
Looking
Upgradient
Water Level
Bedrock
Contact
Notes: Review of the acidity in Live Oak

## Slide 8: Site Layout
MW
MWVZ01
Still Well
Neutral Water
Mix Tank
Weir
Tank
(solids retention)
A
Pump
Totalizer
A – Mix Tank
B – Weir Tank
C – Basin
Well
Flow
Direction
Legend
*Diagram not to scale
N
B
C
X
Milk of Lime
Basin
Gravity
Feed
Groundwater
Flow

## Slide 9: Weir Tank Schematic
In
Out
FLOW
Solids trapped behind weir

## Slide 10: Test Results
Implementability
  mix near-solubility lime solution
  control solids
  avoid application facility/aquifer formation damage
Effectiveness
  raise pH
  reduce metals concentrations

## Slide 11: Test Results
Implementability
  mix near-solubility lime solution
  control solids
  avoid application facility/aquifer formation damage
Effectiveness
  raise pH
  reduce metals concentrations

## Slide 12: Alkalinity
Average 1,857 mg/l as CaCO3
NWF Field
NWF Lab

## Slide 13: Test Results
Implementability
  mix near-solubility lime solution
  control solids
  avoid application facility/aquifer formation damage
Effectiveness
  raise pH
  reduce metals concentrations

## Slide 14: SOLIDS CONTROL – WEIR TANK
During Lime Application
Post Neutral Flush

## Slide 15: SOLIDS CONTROL – BASIN DURING ALKALI APPLICATION

## Slide 16
SOLIDS CONTROL – BASIN DURING NEUTRAL WATER FLUSH

## Slide 17: Test Results
Implementability
  mix near-solubility lime solution
  control solids
  avoid application facility/aquifer formation damage
Effectiveness
  raise pH
  reduce metals concentrations

## Slide 18: Infiltration Rate
Average 11.5 gpm

## Slide 19: Test Results
Implementability
  mix near-solubility lime solution
  control solids
  avoid application facility/aquifer formation damage
Effectiveness
  raise pH
  reduce metals concentrations

## Slide 20: Groundwater Quality
Metals concentrations drop by > 90%
pH > 5.3 for 30 days

## Slide 21: Test Summary
Implementability
  Lime solutions near 90% solubility were efficiently mixed with a readily available rental mix tank
  Calcite precipitates were effectively controlled using a readily available rental weir tank
  Lime applied continuously at a rate of 11.5 gpm for 5.14 days
    No clogging of the infiltration basin
    No formation damage
  Basin alkalinity was 98.2% of mix tank alkalinity

## Slide 22: Test Summary
Effectiveness
  Raised aqueous pH at base of treatment volume for >30 days
    maximum pH of 6.58
  Aqueous Al, Cu, and Mn concentrations decreased by >90%
    remained at low levels through end of test (45 days)